## Slide 1
1. Drone follows target vehicle, maintaining visual contact through flight control.
2. Dynamic obstacle avoidance with algorithms ensuring post-avoidance tracking.
3. RGB-based 3D reconstruction, excluding moving vehicle from static scene.
Task Modeling
1. YOLO + AprilTag for tracking and distance control.
Technical Analysis
1 . Multi-view vehicle tracking & distance estimation
2 . RGB-only depth estimation
3 . Obstacle detection & control
4 . LiDAR/sonar-free 3D reconstruction
5 . Dynamic object filtering
Key Challenges
2. DepthAnything for depth estimation, Sobel operator for edge-based obstacle avoidance while tracking vehicle.
3. Mast3r-SLAM for 3D reconstruction, YOLO filters moving objects.
Target-Guided 3D Reconstruction Based on Tello Drone

## Slide 2
CONTENTS
02
AprilTag-Based Tracking with YOLOv11
03
Dynamic Obstacle Avoidance
04
3D Reconstruction System

## Slide 3
AprilTag-Based Tracking with YOLOv11
PART 02
Notes: 优势、yolo、apriltag、飞控

## Slide 4
Benefits of YOLOv11 & AprilTag
Yolo特点
Yolo Features
Adv: Various angles
Disadv: distance estimation is not accurate.
Apriltag Features
Adv: Precise distance measurement from the front
Disadv:Less robust to angle changes
Dual Detection Advantage:
YOLO flexibility + AprilTag accuracy
YOLO extreme
condition testing
Apriltag extreme
condition testing

## Slide 5
Target guide tracking
01
1. Grid overlay
2. YOLO detection
3. Rough distance
measurement
4. Precise distance
measurement
Target information processing
Case 1. with AprilTag
Case 2. without AprilTag
Flight controller matrix
02
Velocity decreases from edges to center
(30cm/s → 0, decreasing 10cm/s per step).
Flight controller matrix
e.g. Located at row 3, column 1, denoted as A(1,3)
At this point, speed_lr= 30 cm/s, speed_ud= 10 cm/s.
Overlay a 7×7 grid
Wicth grid cell containing target
yolo_distance=1416
Apriltag_distance=null
210 mm
240 mm
21 pix
24 pix
f
O
distance
Case1:without AprilTag
yolo_distance=2116
Apriltag_distance=2100
Case2: with AprilTag

## Slide 6
Dynamic
Obstacle Avoidance
PART 03
Notes: depthanything原理、sobel算子障碍判断、壁障实现

## Slide 7
Aprilta特点
DepthAnything & Sobel operator
01
Depth Anything serves as a substitute for depth sensing hardware. Depth values are normalized to the range 0-255
Depth Map Creation
02
“Ground” depth maps show linear variation with distance (left). Horizontal slicing reveals that most areas have minimal gradient change, while significant changes indicate obstacles (right).
Sobel operator obstacle detection
Employs knowledge distillation: a teacher model trained on large labeled datasets guides a smaller student model to achieve the same task with minimal accuracy loss.
Sobel is a gradient-based edge detector using X and Y directional gradients. Here, only the horizontal filter is applied.
comparison between the depth map and obstacle detection map.
Test case 1
Test case 2
Test case 3
LiDAR dataset
T
Teacher model（T）
Train
inference
T’s Generated dataset
Color jitter
Gaussian blur
CutMix
Noise
Train
S
Student model（S）
Test case 1
Test case 2
Test case 3

## Slide 8
3D Reconstruction System
PART 04

## Slide 9
MASt3R-SLAM
Principle & improvements
Initialization
stage
Creates the first keyframe and initial map by processing the first frame through MASt3R to generate pointmap and encoded features.
Tracking stage
Estimates current frame pose through efficient pointmap matching with recent keyframes and performs local map fusion.
Relocalization
stage
Recovers tracking by matching current frame against the global map database when tracking fails or error accumulates.
Three stages of MASt3R-SLAM
Challenge: Dynamic objects impact static environment
Moving objects interfere with vehicle-guided drone mapping by causing feature matching errors that deform static point clouds.
Solution: Vehicle Removal
Expand YOLO detection region by 3 pixels outward and apply a transparent mask over the vehicle area.
Use alpha channel to convert input image to RGBA format
Adjust initialization to skip tracking phase for masked regions
Set confidence to 0 in masked areas
Implementation: Add Alpha Channel